| CHEMICAL & PROPERTIES | HEALTH HAZARD | FIRE & REACTIVITY HAZARD | SPILLS & LEAK HAZARD | FIRST AID |
| --- | --- | --- | --- | --- |
| 1. AMMONIA (NH3) Colourless gas Pungent Odour Melting point- 770C Boiling Point – 330C Auto ignition - Temp.- 6510C Vapour density 0.597 Explosive limit - % by Vol Lower - 16 Upper - 25 TLV : 25 ppm | Avoid inhalation & body contact can be fatal Irritation of Eyes, Nose & throat. Coughing and Vomiting, Cold Burn due to liquid Use respiratory Protection. | Can catch fire. Hazard is moderate when exposed to heat Or flame. Lightly reactive. Wear full Protection. | Great danger of Fire, Explosion or gas cloud. Wear full protection along with BA set or online respirator in the Spill area. Stay upwind. Keep people away. Avoid body body Contact. Minimise rising cloud By water spray. | INHALATION Remove victim to fresh Air, Inhale vapour of Worm water and give Artificial respiration. EYE CONTACT Wash with plenty of water or solution of 0.5 to 1% Alum. SKIN CONTACT Wash with plenty of water & apply a lotion consisting of 5% solution of acetic citric, tartaric or Salicylic acid. |
| 2. CHLORINE (Cl2) Greenish yellow gas. Molecular weight 70.9 Melting point - 1010C Boiling point - 34.50C Density – 1.47 Vapour Density 2.49 TLV : 1 ppm | Dangerous gas. Can be fatal. Extremely irritant to eyes, nose & throat.Vapour can be cause headache, coughing, pain in the body. Breathing may reach to point where death is possible by suffo- cation. Wear full protection along with BA set or Online respirator. | Fire hazard is moderate. Can reach to cause fire or explosion if comes in contact with Turpentine, Ammonia and Hydrocarbons. | Shut of the outlet of Leakage if possible. Ensure the running of the absorption system. Wear full protection along with BA set or online respirator in the spill area. Stay upwind. Keep people away. Avoid body contact. Minimize rising cloud By water spray. | INHALATION Removing victim to fresh Air and give artificial respiration. EYE&SKIN CONTACT Wash with plenty of Water. Remove Contaminated clothing. |
| 3. SULPHURIC ACID (H2SO4) Colourless liquid, Solubility in water. Boiling point – 2900C Melting point – 10.50C Specific gravity – 1.84 Odour less, miscible with alcohol | Inhalation may Injure lungs, Ingression or contact with skin caused severe burns | Emits tonic Fumes of SOx; Hazardous Combustion Reactive & Corrosive in Nature. | Shut of the outlet of Leakage if possible. Ensure the running of the absorption system. Wear full protection Of PVC suit & shoes. Dozing of lime in Spillage area. Keep people away. Avoid body contact. Diluted by water spray. | INHALATION Removing victim to fresh Air and give artificial respiration. EYE&SKIN CONTACT Wash with plenty of Water. Remove contaminated clothing |
| 4. PHOSPHURIC ACID ( H3PO4 ) Thick liquid, soluble in Water. Odour- pleasant Boiling point - >1300C Specific gravity – 1.89 | Inhalation may Injure lungs, Ingression or contact with skin caused severe burns | Emits tonic Fumes of POx; Violent reaction With Sodium Te- tra Hydroborate. Reacts with Chlo- -ride+Stainless steel to form Hydrogen gas. | Avoid contact with Liquid or vapours. Provide face shield, Rubber hand gloves, PVC Suit &shoes. | INHALATION Removing victim to fresh Air and give artificial respiration. EYE&SKIN CONTACT Wash with plenty of Water.Remove contaminated clothing |

5.0Chemical  Name:SULPHUR

CAS:7704-34-9

RTECS #:WS4250000

= Wt:100.

Other REC Limits:10 MG/M3

=====================  Hazards Identification

Health Hazards Acute and Chronic:

EYES: SULPHUR DUST IS MILDLY IRRITATING TO EYES.

SKIN: UPON CONTINUED OR REPEATED CONTACT MAYCAUSE IRRITATION OF THE SKIN.

INHALATION: INHALATION OF DUST CAN CAUSE RESPIRATORY TRACT IRRITATION.

INGES TION: SULPHUR HAS A LOW ORDER OF TOXICITY.

Effects of Overexposure:EYES:  MILD IRRITATION.

SKIN: IRRITATION.

INHALATION: RESPIRATORY TRACT IRRITATION.

INGESTION: SULPHUR HAS A

LOW ORDER OF TOXICITY.

=======================  First Aid Measures

First Aid:EYES: RINSE WITH WATER FOR 10-15 MINUTES. CONSULT A PHYSICIAN SHOULD IRRITATION PERSIST.

SKIN: WASH WITH SOAP AND WATER. CONSULT . A PHYSICIAN SHOULD SYMPTOMS OR IRRITATION OCCUR.

INHALTION: MOVE  PERSON  TO FRESH AIR. IF SYMPTOMS OR IRRITATION OCCUR, SEE PHYSICIAN. INGESTION: IF LARGE AMOUNTS ARE SWALLOWED, IMMEDIATELY GET MEDICAL HELP.

=====================  Fire Fighting Measures

Flash Point:=207.C, 404.6F

Autoignition Temp:=232.C, 449.6F

Lower Limits:35 G/M3

Upper Limits:1400 G/M3

Extinguishing Media:WATER FOG, STEAM, CARBON DIOXIDE. EXTINGUISH SMALL FIRES BY GENTLY COVERING WITH SAND OR FINE EARTH TO EXCLUDE OXYGEN.

Fire Fighting Procedures:WEAR SELF-CONTAINED BREATHING APPARATUS. WATER STREAM MAY SPLATTER MOLTEN SULFUR.

Unusual Fire/Explosion Hazard:DUST OR VAPORS CAN FORM EXPLOVE MIXTURE  WITH AIR.

==================  Accidental Release Measures

Spill Release Procedures:USE NORMAL CLEAN-UP PROCEDURES FOR SPILLS.( MECHANICAL SWEEPING OR VACUUM DEVICES NOT RECOMMENDED.)

ELIMINATE SOURCES OF POSSIBLE IGNITION.  AVOID UNNECESSARY DUSTING.

=============  Exposure Controls/Personal Protection  =============

Respiratory Protection:WHERE EXPOSURE TO THE DUST IS APPARENT, A

HALF-FACE DUST/MIST RESPIRATOR MAY BE WORN.

Ventilation:DILUTION VENTILATION IS A SATISFACTORY CONTROL. IF

CONDITIONS CREATE DISCOMFORT TO WORKER, LOCAL EXHAUST SYSTEM SHOULD BE CONSIDERED.

Protective Gloves:PROTECTIVE GLOVES

Eye Protection:WEAR SAFETY GLASSES

Other Protective Equipment:CLEAN BODY COVERING CLOTH

Supplemental Safety and Health

SYNONYMS: SULFUR, FLOWERS OF SULPHUR.