MATERIAL SAFETY DATA SHEET

1.   CHEMICAL IDENTITY

Chemical Name:  PHOSPHORIC ACID       Chemical Classification:  Inorganic  Acid

Synonyms         :  Ortho Phosphoric Acid      Trade Name :

Formula : H3PO4 	         C.A.S. No.: 7664-38-2	          	   U.N.No. :  1805

Regulated Identification  : Shipping Name : Phosphoric Acid,   Hazchem Code : 2R

: Codes / Label   : Corrosive , Class  8

: Hazardous Waste ID No.  : 16

HAZARDOUS INGREDIENTS:       CAS No.           HAZARDOUS  INGREDIENTS :

1.   Phosphoric Acid                      7664-38-2           3.

2.                                                                               4.

2.   PHYSICAL / CHEMICAL DATA

Boiling point / Range oC  :  > 1300 C                 Physical   :  Thick Liquid  / Solid

Appearance  :  Colourless                                 Odour       :   Pleasing

Melting / Freezing Point 0C : 42.40C                 Vapour Pressure :@ 350C 0.286 mm

Hg at 200C

Vapour Density  :                                              Solubility : Soluble in water

( Air = 1)                                                            Others    :  Others soluble in Alcohol

Specific Gravity  : 1.89 at  25oC                         pH         :  1.5  ( 0.1 N)

(Water = 1)

3.FIRE / EXPLOSIVE HAZARD DATA

Flammability  :   No                 LEL Not pertinent %                   Flash Point 0C  :  Not

Pertinent (OC)

TDG Flammability  : 8             UEL Not pertinent %                   Flash Point  oC :  Not

Pertient (CC)

Autoignition Temperature oC                 :   Not Applicable

Explosion sensitivity to impact               :  Stable

Explosion sensitivity to static electricity : Data not available

Hazardous Combustion Products          : Emits Toxic fumes of Pox

Hazardous Polymerization                     : Will not occur

Combustible Liquid  : No       Explosive Material  : No          Corrosive material   : Yes

Flammable Material : No       Oxidiser    : No                         Others  :

Pyrophoric Material  : No       Organic Peroxide : No

___________________________________________________________________

4.    REACTIVITY DATA

Chemical Stability				:  Stable

Incompability with other material 		:  Strong Caustics, Most Metals

Reactivity  :   Potentially violent reaction with Sodium Tetrahydroborate

Hazardous Forms : Reacts with Chlorides + Stainless Steel to form explosive

Reaction Product                                            Hydrogen gas.

: Explosive mixtures with Nitromethane

5. HEALTH HAZARD DATA

Routes of Entry       : Inhalation,Ingestion Eyes & Skin.

Effects                     : Burns on mouth and lips,sour acid taste,severe gastrointestinal

Irritation,nausia

Exposure /

Symptoms               : vomiting,bloddydiarrhea,difficult swallowing,severe abdominal

Pains,thirst,academia,difficult breathing,convulstons,collapse,

Shock and death.

Emergency              : Ingestion : Do not induce vomiting,give water,milk or vegetable

Treatment                                   oil.

Skin & Eyes : Flush with water for at least 15 minutes,seek

Medical aid.

LD50 (oral-rat)     : 1530 mg / kg

Mg/m3

Permissible exposure limit : 0.25 ppm / 1 mg/m3          Odour Threshold :  Not

TLV(ACGIH)                       : 0.25 ppm                          STEL :  0.75 ppm / 3 mg / m3

NFPA  Hazard     :        Health                    Flammability                    Reactivity

Special Signals    :           2                                 0                                      0

6. PREVENTIVE MEASURES

Personal              :  Avoid contact with liquid or vapours.

Protective          :  Provide face shield,rubber hand gloves,protective over clothing

Equipment            and shoes.

Handling & Storage

Precaution                 :  Store in well ventilated area away from active material.

7.    EMERGENCY / FIRST AID MEASURES

FIRE    : Not Flammable

FIRE EXTINGUISHING  MEDIA

Special Procedure : Keep the containers cool by spraying water if exposed to

Heat or flame.

Unusual Hazards   :  Flammable gas is produced on contact with metals.

EXPOSURE  : First Aid Measures : If ingested,do not induce vomiting,give milk,water

and vegetable oil.If skin and eyes are affected flush with plenty of

water.Seek medical aid immediately.

Antidote / Dosages : Not Available

SPILLS:

Steps to be taken                  : Neutralise with alkali and dilute and drench with water.

Waste Disposal Method        : Seal all waste in vapour tight plastic bags for eventuate

disposal.

8.    ADDITIONAL INFORMATION  /  REFERENCES

A Human poison by an inspecified route.Toxic by ingestion and skin contact.Used to

manufacture of fertilizers,detergents,food beverages and for water treatment.

9.    MANUFACTURES / SUPPLIERS DATA

NAME OF FIRM     :          Contact person in Emergency

MAILING ADDRESS

TELEPHONE / TELEX NOS

TELEPHONIC ADDRESS      : Local Bodies involved standard packing TREM card

Details  / Ref.

___________________________________________________________________

10.   DISCLAIMER :

Information contained in this material data sheet is believed to be reliable but no representation,guarantee or warranties of any kind are made as to its accuracy,suitability for a particular application or results to be obtained from them.It is upto the manufactured / handled or sold by him as the case may be.The I.C.M.A. makes no warranties expressed or implied in respect of the adequacy of this document for any particular purpose.

MATERIAL SAFETY DATA SHEET

1.  IDENTITY OF MATERIAL

| Product Name | Ammonia | Chemical |  |
| --- | --- | --- | --- |
| Trade Name | Ammonia | Designation Synonyms | Anhydrous Ammonia |

Formula              Label / Class            Category       CAS Number       UN  Number

| NH3 |  |  | 7664-41-7 | 1005 |
| --- | --- | --- | --- | --- |
| Regulated Identification | Shipping Codes / Lebel |  | HAZCHEM Code | 1005-15 |
|  | Hazardous waste Identification Number | Nil |  |  |
|  | Hazardous Ingredients |  | CAS Number |  |
| 1 | Nil |  | - |  |

2. PHYSICAL AND CHEMICAL PROPERTIES

| Physical State | Boiling Point ( oC) | Vapour pressure (mm-Hg) @ 35oC |
| --- | --- | --- |
| Liquid / Gaseous | - 33.3 | > 1 atm. |
| Appearance | Melting / Freezing Point ( Oc) | Evaporation rate @ 30 oC |
| Colourless | - 77.7 |  |
| Odour | Vapour Density(air =1) | Solubility in water @ 300C |
| Penetrating Pungent Suffocating | 0.6 | Highly Soluble |
| Others (Corrosivity etc.) | Specific Gravity (Water =1) | pH |
|  | 0.77 | 11.7 |

3.   FIRE AND EXPLOSIVE HAZARDS DATA

| Explosion / Flammability | Flash Point (oC) | LEL (%) | Auto ignition Temperature (0C) |
| --- | --- | --- | --- |
| Yes |  | 16 | 651 |
|  |  | UEL (%) | TDC Flammability (Classification) |
|  |  | 25 |  |

4.   REACTIVE HAZARDS

| Stability To | Impact(Hazardous Combustion Products) | Nil |
| --- | --- | --- |
|  | Static Discharge(Hazardous Decomposition Product) | Nil |
|  | Reactivity ( Conditions to avoid) | Reactive with chlorine,violent reaction with acids,strong oxidants,halogens,highly soluble in water generating heat. |
| Hazardous Polymerization | May / May not occur (Conditional to avoid) | Nil |
| Incompability | Materials to avoid | Strong oxidizers,hypo chlorite bleaches,mercury chlorine,nitrogen oxide,halogens,Aluminium,Zinc,Copper etc. |

5.   HEALTH HAZARD DATA

| Routes of Entry | Eyes, Respiratory tract and skin contact. |
| --- | --- |
| Effects of Exposure / Symptoms | Liquid ammonia causes cold burns on contact. 400-700 ppm causes upper respiratory tract irritation. 1000-2000 ppm causes severe coughing,severe eye,nose and throat irritation. 3000 – 4000 ppm could be fatal after 30 minutes exposure. |
| LD 50(rat) (mg / kg of body wt.) |  | LC 50 (rat) Mg / ¼ hours. |  |
| (Orally or percutaneous absorption ) |  |
| Permissible Exposure Limit ( PEL) | ppm |  | Short Term Exposure Limit(STEL) | ppm | 35 |
|  | Mg/Cu. m |  |  |  |  |
|  |  |  |  | Mg/Cu.m. | 28 |
| Threshold Limit Value (TLV) of ACIGH | Ppm | 25 | Odour Threshold | ppm |  |
|  | Mg/Cu.m | 17 |  |  |  |
| Emergency Treatment |  |

6.   HAZARD SPECIFICATION

| NFPA Hazard | Signal | Health | Flammability | Stability | Special |
| --- | --- | --- | --- | --- | --- |
| 49 | Gas & Liquid | 2 & 3 | 3 | 0 | - |
| Known Hazards |  |  |
| Combustible Liquids | Water reactive Material | Irritants |
| No | - | - |
| Flammable Material | Oxidiser | Sensitizer |
| Yes | - | - |
| Pyrophoric Material | Organic Peroxide | Carcinogen |
| No | - | - |
| Explosive Material | Corrosive Material | Mutagen |
| Unstable Material | Compressed Gas | Others (Specify) |

7.    SAFE USAGE DATA

| Ventilation | General / Mechanical |  |
| --- | --- | --- |
|  | Local Exhaust |  |
| Protective | Eyes (Specify) |  |
| Equipment | Respiratory (Specify) | Breathing Apparatus Set |
| Required | Gloves (Specify) | Hand Gloves |
|  | Clothing (Specify) |  |
|  | Others (Specify) | Body protective Suit |
| Precautions | Handling & Storage | To be stored in recommended vessels. |
|  | Others (Specify) | Handle with the use of PPE only. |

8.   EMERGENCY RESPONSE DATA

| Fire | Fire Extinguishing Media | Water,Alkaline Foam |
| --- | --- | --- |
|  | Special Procedures | Water Curtains |
|  | Unusual Hazards | Spills |
| Exposure | First Aid Measures | Any person affected by ammonia should be taken immediately into fresh air. Eyes should be washed with an abundance of clean water for at least fifteen minutes. Any contaminated cloths with ammonia liquid should be drenched with water & be removed as soon as possible and affected point should be washed with copious amounts of water. Patient should be kept warm. Administer oxygen if available in case of difficult breathing or give artificial respiration. Must be consulted with doctor. |
| Spills | Steps to be taken | To be contained and mitigated with alkaline. Foams for avoiding rapid evaporation. |
|  | Waste Disposal Method |  |

9.  ADDITIONAL INFORMATION

Ammonia is used as an intermediate for Diammonium Phosphate or Mixed Fertiliser Production at IFFCO Paradeep.

10.    SOURCES USED

Referrence to books,journals, etc.

Irvin Sax  ( Dangerous Properties of Chemicals)

11.   MANUFACTURERS / SUPPLIERS  DATA

| Firms Name | Overseas Suppliers ( By Ships) |
| --- | --- |
|  | Standard Packing |
| Mailing Address |  |
| Telephone Number |  |
| Telex Number |  |
| Telegraphic Address |  |
| Contact person in Emergency |  |
|  | Others |
| Emergency Telephone In Transit Areas. |  |

MATERIAL SAFETY DATA SHEET

1.  IDENTITY OF MATERIAL

| Product Name | Chlorine | Chemical | Inorganic gas or liquid |
| --- | --- | --- | --- |
| Trade name | Chlorine | Designation Synonyms | None |

Formula              Label / Class        Category             CAS Number       UN Number

| Cl2 |  |  | 7782-50-5 | 1017 |
| --- | --- | --- | --- | --- |
| Regulated Identification | Shipping codes / Label Hazardous waste identification Number | Non-Flammable gas,poison class 2 | HAZCHEM No / Code | 1017-20 |
|  |  | 17 |  |  |
|  | Hazardous Ingredients |  | CAS Number |  |
|  | Chlorine |  | 7782-50-5 |  |

2.  PHYSICAL AND CHEMICAL PROPERTIES

| Physical State | Boiling Point (0C) | Vapour Pressure (mm-Hg) @ 350C |
| --- | --- | --- |
| Gas / Liquid | (-) 34.5 | > 1 atm. ( 4800 ) |
| Appearance | Melting / Freezing Point (0C) | Evaporation rate @ 30oC |
| Green Yellow Gas |  |  |
| Odour | Vapour Density ( air = 1) | Solubility in water @ 300C |
| Suffocating | 2.49 | Insoluble |
| Others (Corrosivity etc.) | Specific Gravity (Water = 1 ) | pH |
| Corrosive | 1.47 | na |

3.   FIRE AND EXPLOSIVE HAZARDS DATA

| Explosion / Flammability | Flash Point(oC) | LEL (%) | Auto Ignition Temperature (oC) |
| --- | --- | --- | --- |
| No |  |  |  |
|  | Flash point (oC) | UEL (%) | TDC Flammability (Classification) |
|  | - | - | - |

4.  REACTIVE HAZARDS

| Stability to | Impact (Hazardous Combustion Products) | Toxic product are generated and combustible burn in Chlorine |
| --- | --- | --- |
|  | Static Discharge (Hazardous Decomposition Product) | Stable |
|  | Reactivity (Conditions to avoid ) | Reaction with alcohol metals, Sulphites,trialhilboranes |
| Hazardous Polymerization | May / May not occur (Conditional to avoid ) | May not occur |
| Incompatibility | (Materials to avoid ) | Combustible substances, Finally divided metals. |

5.    HEALTH  HAZARD  DATA

| Routes of Entry | Eyes,Respiratory tract and skin contact. |
| --- | --- |
| Effects of Exposure / Symptoms | Causes eye irritation,sneezing,copious salivation,general excitement and restlessness.High concentration causes respiratory distress and violent coughing.Often with retching.Death may result from suffocation. 30 ppm causes intense coughing fits & burning. 40 ppm causes cardiac paralysis & bronchitis. 1000 ppm danger to life even after few deep inhalation. |
| LD 50 (rat) (mg / kg of body wt.) | Not listed | LC 50 (rat) Mg / ¼ hours | Not listed |
| (Orally or percutaneous absorption ) |  |  |
| Permissible Exposure Limit (PEL) | ppm 1 | Short Term Exposure Limit (STEL) | ppm 3 |
|  | mg / cu.m. 3 |  | Mg / cu.m. 9 |
| Threshold limit value (TLV) of ACGIH | ppm 1 | Odour Threshold | ppm 3.5 |
|  | mg / cu.m. 3 |  | mg./cu.m. 10.2 |
| Emergency Treatment | Inhalation : Remove the victim to fresh air area,support respiration,give oxygen,if necessary.Eyes : Flush with large amounts of water for at least 15 minutes.Seek medical aid immediately. |

6.    HAZARD SPECIFICATION

| NFPA Hazard | Signal | Health | Flammability | Stability | Special |
| --- | --- | --- | --- | --- | --- |
|  |  | 3 | 0 | 0 | - |
| Known Hazards |  |  |
| Combustible Liquid | Water Reactive material | Irritant |
| No | No |  |
| Flammable Material | Oxidiser | Sensitizer |
| No | Yes |  |
| Pyrophoric Material | Organic Peroxide | Carcinogen |
| No | No | No |
| Explosive Material | Corrosive Material | Mutagen |
| No | Yes |  |
| Unstable Material | Compressed Gas | Others ( Specify) |
| No | Yes |  |

7.  SAFE USAGE DATA

| Ventilation | General / Mechanical | Well ventilated area preferably with a hood with forced ventilation. |
| --- | --- | --- |
|  | Local exhaust | Tonners should always be handled,using a lifting clamp,cradle or carrier. |
| Protective Equipment Required | Eyes ( Specify) | Head Mask |
|  | Respiratory (Specify) | SCBA |
|  | Gloves ( Specify ) | Hand Gloves PVC |
|  | Clothing (Specify ) | Rubber over Coat |
|  | Others ( Specify) | Gumboots |
| Precautions | Handling & Storage | Storage in well ventilated areas or outdoors. |
|  | Others ( Specify) | Protect against physical damage. Separation from combustible organic or easily oxidisable material. Isolate from Acetylene,Ammonia, Hydrogen,Hydrocarbons,Ether,Turpentine & finely divided material. |

8.  EMERGENCY RESPONSE DATA.

| Fire | Fire extinguishing Media | Water |
| --- | --- | --- |
|  | Special procedures | Water curtains |
|  | Unusual Hazards | Poisonous gases emitted on burning |
| Exposure (Inhalation,skin,eye contact and ingestion ) | First Aid Measures | Evacuate the contaminated zone Call a Doctor. Affected clothing should be removed and skin should be washed thoroughly with water. In case of unconsciousness transport him to a quiet place and keep him warm.Inhale oxygen or give artificial respiration till doctor arrive. Wash thoroughly on contaminated area of the body. |
| Spills | Steps to be taken | Shut off leaks if without risk.Contain liquid with sand or earth.Prevent the liquid from entering the sewer.Vapours create toxic atmosphere.Knock down vapours with water spray. |
|  | Waste Disposal Method | Neutralize small liquid spillages with soda ash and drain with abundant water.Cover pool with protein foam.So that the release of vapour to atmosphere is low and under control. |

9.   ADDITIONAL INFORMATION

In case of large gas escapes,the presence of cloud can be marked with ammonia with which it will turn into a mist.Run away from the gas clouds in a direction perpendicular to the wind direction.Avoid liquid chlorine from leaking and body contact.Person with pulmonary diseases should avoid the exposure.A concentration of 3.5 ppm produces a detectable odour .15 ppm causes immediate irritation of throat.Concentration of 50 ppm are dangerous for even short exposures.1000 ppm is fatal.Can react to cause fires / explosion on contact with turpentine,illuminating gas,polypropylene,Rubber,Sulfamic acid,Acetaldehyde,Alcohols.Bring the leaking portion of the cylinder to the uppermost position,so that only the gas escapes and not the liquid.

10.   SOURCES USED

Reference to books,Journals, etc.

Irrvin Sax  ( Dangerous properties of Chemicals )

11.  MANUFACTURERS /  SUPPLIERS DATA

| Firms Name |  |
| --- | --- |
|  | Standard Packing |
| Mailing Address |  |
| Telephone Numbers | Others |
| Telex Number |  |
|  | Others |
| Telegraphic Address |  |
| Contact person in Emergency |  |
|  | Others |
| Emergency Telephone in Transit Areas |  |

MATERIAL  SAFETY DATA SHEET

1. IDENTITY OF MATERIAL

| Product name | Sulphuric Acid | Chemical | Inorganic Acid |
| --- | --- | --- | --- |
| Trade Name | Sulphuric Acid | Designation Synonyms | Oil of vitrol,Battery acid,Chamber acid, Spent sulphuric acid |

Formula              Label / Class         Category                  CAS Number      UN Number

| H2SO4 | Corrosive,Class 8 |  | 7664-93-9 | 1830 |
| --- | --- | --- | --- | --- |
| Regulated Identification | Shipping Codes / Label | Sulphuric Acid, Corrosive,Class 8 | HAZCHEM Code | 2P |
|  | Hazardous Waste Identification Number | 16 |  |  |
|  | Hazardous Ingredients |  | CAS Number |  |
| 1 | Sulphuric Acid |  | 7664-93-9 |  |

2.  PHYSICAL AND CHEMICAL PROPERTIES :

| Physical State (Gas,Liquid,Solid) | Boiling Point (0C) | Vapour Pressure (mm-Hg)@ 1450C |
| --- | --- | --- |
| Liquid | 290 | 1 |
| Appearance | Melting / Freezing Point (0C) | Evaporation Rate @ 300C |
| Colourless Oily | NA | NA |
| Odour | Vapour Density (air =1) | Solubility in water @ 300C |
| Odorless | 3.4 | Visible |
| Others (Corrosivity ) | Specific Gravity (Water =1) | pH |
| Corrosive | 1.84 | Less than 1 |

3.  FIRE AND EXPLOSIVE HAZARDS DATA

| Explosion / | Flash Point (0C) | LEL (%) | Auto Ignition Temperature (0C) |
| --- | --- | --- | --- |
| Flammability |  |  |  |
|  | Flash Point (0C) | UEL (%) | TDC Flammability (Classification) |
| NA |  |  |  |

4.   REACTIVE HAZARDS

| Stability to | Impact (Hazardous Combustion Products) | Emits toxic fumes of SO2 |
| --- | --- | --- |
|  | Static Discharge (Hazardous Decomposition Products) | Stable |
|  | Reactivity (Conditions to avoid ) | Powerful Oxidiser |
| Hazardous Polymerization | May / May not occur (Conditional to avoid ) | May not occur |
| Imcompability | Materials to avoid | Organic Chlorates,Carbides,Fulminates, Picrates and metals. |

5.   HEALTH  HAZARD  DATA

| Routes of Entry | Inhalation,Ingestion,eyes |
| --- | --- |
| Effects of Exposure/ Symptoms | Inhalation of vapour from hot concentration acid may injure lungs. Swallowing may cause injury or death. Contact to skin or eyes causes severe burns. Dilute solution cause dermatitis. Exposure cause bronchitis. |
| LD 50 (rat) (mg/kg of body weight | 2140 | LC 50 (rat) Mg / |  |
| (Orally or percutaneous absorption) |  |  |  |
| Permissible Exposure Limit (PEL) | ppm |  | Short term exposure limit (STEL) | ppm |  |
|  | Mg/cu.m | 1 |  | Mg/cu.m |  |
| Threshold Limit value (TLV) of ACGIH | ppm |  | Odour Threshold | ppm |  |
|  | mg/cu.m | 1 |  | mg/cu.m | 1 |
| Emergency Treatment | Observe victim for delayed pulmonary reaction. Move the victim to fresh air. Give artificial respiration. Skin: Remove cloths & shoes. Do not use oil or ointment. Flush affected area with plenty of water. Eyes: Wash with plenty of water for fifteen minutes. Ingestion: Give plenty of water to drink. Do not induce vomiting. Seek medical aid. |

6.    HAZARD  SPECIFICATION

| NFPA Hazard | Signal | Health | Flammability | Stability | Special |
| --- | --- | --- | --- | --- | --- |
|  |  | 3 | 0 |  |  |
| Known Hazards |  |  |
| Combustible Liquid | Water reactive Material | Irritant |
| No | Yes | Yes |
| Flammable material | Oxidiser | Sensitizer |
| No | Yes |  |
| Pyrophoric material | Organic Peroxide | Carcinogen |
| No | NO | No |
| Explosive materials | Corrosive Materials | Mutagen |
| No | Yes |  |
| Unstable Material | Compressed Gas | Others ( Specify) |
| No | No |  |

7.     SAFE USAGE DATA

| Ventilation | General / Mechanical |  |
| --- | --- | --- |
|  | Local Exhaust | Wall ventilated place away from oxidizer. |
| Protective Equipment Required | Eyes ( Specify) | Safety goggles, face shield |
|  | Respiratory ( Specify) | Self contained or air line breathing apparatus |
|  | Gloves ( Specify) | Rubber |
|  | Clothings ( Specify) | Rubber apron |
|  | Others ( Specify) | Rubber shoes,Safety shower, Eye wash fountain |
| Precautions | Handling & Storage | Store in cool,well ventilated place away fron oxidizes,acids of 98% are to be stored in MS or CI tanks / drums. |
|  | Others ( Specify) | SafetyShowers,eye wash fountains. |

8.   EMERGENCY RESPONSE DATA

| Fire | Fire Extinguishing Media | DCP / CO2 Do not use water |
| --- | --- | --- |
|  | Special Procedures | Keep containers cool by spraying water if exposed to flame or heat |
|  | Unusual Hazards | Poisonous gases may be produced |
| Exposure (Inhalation,skin,eye contact & ingestion) | First Aid measures | If inhaled,remove the victim to fresh air,provide artificial respiration or oxygen if required, If eyes are affected wash with plenty of water for 15 minutes or more.If skin is affected remove contaminated cloths and shoes & wash the affected area with plenty of water and soap. Seek medical help immediately. |
| Spills | Steps to be taken | Shut off leaks if without risk. Contain leaking liquid on sand or earth.Do not absorb on saw dust or other combustibles. |
|  | Waste Disposal Method |  |

9.   ADDITIONAL INFORMATION

Sensitivities to Sulphuric acid mists or vapours vary with individuals.Normally 0.125 to 0.5 ppm may be mildly annoying 1.5 to 2.5 ppm may be definitely be unpleasant,10 to 20 ppm unbearable.Contact with water violent reaction generating much heat and splattering of hot acid.Attacks many metals.Liberating hydrogen which is flammable & forms explosive mixture with air.

10.  SOURCES USED

____________________________________________________________________

Reference to books,Journals,etc

India Chemical manufacturer association publication

Irvin Sax  ( Dangerous Properties of Chemicals )

11.  MANUFACTURERS / SUPPLIERS DATA

| Firms Name | IFFCO Paradeep ( Intermediate Product for Phosphoric Acid Manufacture ) |
| --- | --- |
| Mailing Address | paradeep@iffco.nic.in |
| Telephone Number | 06722-223345 |
| Telex Number | 06722 - 222857 |