Sub.  :  LIST OF  suggestions Awarded on  26th January Celebration , 2010 :

| Sl. No. | Name, P.No. & Designation | Dept. | Brief Description of Suggestion. | Suggestion No. | Award Amount (in Rs.) |
| --- | --- | --- | --- | --- | --- |
| 1 | Mr Naresh Chandra Swain, Asst. Manager (Mech) P. No. 108539 | DAP (Mech) | Fines Conveyor Gear Box/ Driving chain: High capacity gear box with triplex chain to be installed to reduce frequent break down. | SS/ 171 | 501 |
| 2 | Mr. Jyoti Ranjan Swain, Sr. Engineer (Mech) P.No. 108803 | PAP (Mech) | Transfer Conveyor of Ball Mill-“C” Removing transfer conveyor-C & making one horizontal weigh feeder conveyor at inclined position from weigh feeder gate of Ball Mill-“A” spillage & dust problem will be reduced. | SS/179 | 1001 |
| 3 | Mr Ranjan kumar Patanaik, Sr. Engineer, P.No. 108536 | Energy Centre | All Drain system is to be improved by providing wide Slab covered drains with proper slope. | SS/193 | 251 |
| 4 | Mr Jafar Saheb, Engineer, P.No. 109102 , | SAP (process) | Boiler Area in SAP 1 & 2 Plants. Provision of Direct DM Water line to both Trains SAP- I &II Steam drums, by taking tapping before the addition of return condensate line will accelerate rate of cooling. | SS/ 203 | 251 |
| 5 | Mr Chandra Kanta Barik, Asst. Operator, P.No. 108264 | PAP Process | G- evaporator sump & reactor sump pumps discharge line to be connected directly to spillage sump, to avoid reactor drain choking. | SS/236 | 251 |
| 6 | Mr KGKV Prasad Rao, Dy. Manager (P. No. 108530) | DAP (Mech) | DAP- Granulator: By removing the Oil Tank (Reservoir) and connect the pump suction to the gear box out let directly will avoid failures. | SS/ 240 | 501 |
| 7 | Mr Durgesh Vatsa, Sr. engineer , P.No. 109227 | Power Plant | By implementing stay put mechanism in control valves, when ever instrument air fails, the valve will remain in the same position in which it was operating earlier. | SS/ 253 | 251 |
| 8 | Mr B D Jadav, Sr. Managere P.No. 102603 | (O&U) | HIC 503 & HIC 504 may be operated automatically with increase /decrease in tank Pr. With slight change/modification by I/M. Its opening Pr may be set about 150 mm wc less than RV Popping Pr & should close at 500 mm wc. | SS/257 | 501 |
| 9 | Mr Bharat Chandra Das, Jr. Operator, P. No. 108788 | PAP Process | A concrete wall of 200 mm High required near pad cleaning area. A plat form required near H2SO4 line battery limit valve & its drain valve for safety & easy operation. | SS/260 | 251 |
| 10 | Mr Prasant Kumar Behera , Asst. Operator, P- 108275 | DAP (Production) | Production Unit Down time & Plant load improvement : Vibrators are required at Product Surge Hopper for smooth flow of product. (Electrical or Pneumatic) | SS/ 261, | 251 |
| 11 | Mr. Umesh Mahapatra, Rigger (P.No.107700) | DAP (Mech) | DAP- Fines Conveyor take up - Counter Weight bucket is to be made close type and side welding with guide channels modification will reduce breakdowns. | SS/262 | 251 |
| 12 | Mr Chandra Kanta Barik, Asst. Operator, P.No. 108264 | PAP (Process) | Filtration area – Product seal tank ladders base to be provided concrete base because acid water damage the base of ladders. Filters A, B, C, D 3rd wash 4th seal tanks platform to be provided & E,F & G all seal tank platform to be provided & also railing to be provided for safety purpose. Cake wash tank ladder to be modified as covered types for safety purpose. | SS/ 265 | 251 |
| 13 | Mr Prasant Kumar Behera , Asst. Operator, P- 108275 | DAP (Production) | Wash Liquor to Primary Scrubber tank line : Wash Liquor to Primary Scrubber tank line to be modified. It may be laid in the pipe rack & just adjacent of the weak acid to primary scrubber tank line. This line will reduce four elbows, the line will not get choked early as comparable as prior line & it reduce cleaning cost. | SS/ 270 | 501 |
| 14 | Mr Giridhar Chaturvedi, Sr. Engineer, P.No. 108777 | (O&U) | Un insulated hot condensates return pipe line (surface temperature without insulation is 70-75 deg. C approx.) must be properly insulated for providing personnel protections. | SS/273 | 251 |
| 15 | Mr Prasant Kumar Behera , Asst. Operator, P- 108275 | DAP (Production) | Permanent MS line to be provided : Permanent MS line to be provided from wash liquor pump discharge to pre scrubber tank. It will help to reduce down time whenever there is no flow or less flow from primary scrubber to pre scrubber. | SS/ 276 | 501 |
| 16 | Mr B R Battani , Jr. Technician, P.No.107411 | PAP (Process) | PAP Cargo Discharge going in Pipeline. Non Return Valve is required for safe maintenance of the pump. Hydra is not required if platform is made. Job can be done with chain pulley. | SS/ 286 | 251 |
| 17 | Mr Kush Nahak, Asst. Manager (P.no. 109187) | PAP (Process) | Reactor- to maintain the SO4, P2O5, Solid content & Temp. By charging all mixing tees SO4 level, P2O5 temperature and solid content can be maintained uniformly. | SS/ 288 | 1001 |
| 18 | Mr Ranjan kumar Patanaik, Sr. Engineer, P.No. 108536 | Energy Centre | Condensate line to be routed to AFBC De-aerator or SAP De-aerator to reduce capacity of DM transfer pump & motor. | SS/ 292 | 501 |
| 19 | Mr P K Rout, Ch. Operator, P.No. 108635 | SAP (prod) | Quick identification of Acid Leak at short interval may be possible by installation of Acid leakage Signaling System in Control Room. | SS/295 | 251 |
| 20 | Mr Girija Prasad Naik, Asst. Tech. P.No. 108286 | Instrumentation | Dust extraction system to be provided in each transfer point of conveyors discharge hopper. Instead of hand switches we can operate the gate valves in our total plant by direct air supply with the help of ½ ‘’ ball valve. | SS/ 289 | 501 |
| 21 | Mr Sitaram Pandey, Technician Fitter, P.No. 107716 | Power Plant | TG CW Pump, BRG Top Cover housing I Bolt is required for easy maintenance. | SS/ 300 | 251 |
| 22 | Mr Sitaram Pandey, Technician Fitter, P.No. 107716 | Power Plant | TG I & TG II Condenser Pipe to be provided with some anti corrosive material to prevent corrosion. | SS/ 301 | 251 |
| 23 | Mr Gaurav shukla, Sr. engineer, P.No. 108770 | Power Plant | Boiler feed water pump should be started by DCS (Control Room) in emergency condition when – Running BFP suddenly tripped. Suddenly SAP tripped and extra Steam flow requires. High drum level fluctuation. | SS/ 304 | 501 |
| 24 | Mr. KGKV Prasad Rao, Dy. Manager (108530) & Mahendra Biswal Asst. Tech (Mech.) 108000 | DAP (Mech) | Dryer/ Granulator inching coupling: By Fabricating the clamp & fixing with bolts instead of sliding the coupling will save the time for maintenance. | SS/ 307, | 251 251 |
| 25 | Mr Gaurav Shukla, Sr. engineer, P.No. 108770 | Power Plant | 1. Burner Air: Burner air damper should be operated by DCS and manual damper position should be at same furnace firing floor for easy diesel firing at the time of boiler light up. 2. Air control and oil control of Burner should be operated by DCS for smooth light up BLR. | SS/ 311 | 501 |
| 26 | Mr Arun Kumar Behera , Sr. Engineer (P.No. 108814) | DAP (MAINT) | Standardisation of Primary/Secondary and Product Screen Elevator Gear Box Standardisation of Gear Box of the above drives will reduce the variety and inventory to be maintained. | SS/ 312, | 501 |
| 27 | Mr Ranka Nidhi Panda, Operator, P.No. 108348 | Power Plant | Use of the out let water of Air conditioner (5T) in control room as a cooling media in steam & CBD Sample cooler, the outlet of sample cooler shall be sent to cooling tower sump. | SS/317 | 251 |
| 28 | Mr. K.S. Behera Asst. Mgr. (Inst) P.No. 108503 | Bagging Plant | Automatic System for rejection of Over/Under wt. of bags. During loading of bags to the trucks directly the under/over wt. bags can be separated by implementing a new scheme by using a timer, two pneumatic cylinder and five port solenoid valve. | SS/226 | 501 |
| 29 | Mr. Jyoti Ranjan Swain, Sr. Engineer(Mech) P.No. 108803 | PAP (Mech) | Making another inlet water pipeline to Ball Mill 150-200 mm & Air 1 ½ “ to 2” NB valve with feed spout bend position will reduce choking. | SS/202 | 251 |

.

TN GUPTA

Chairman

Employees Suggestion Scheme